## Slide 1: Latest updates on PoAs rules including multicounty PoAs
Karen Ortega
Regional Workshop (31 August - 2 September), Bogota, Colombia

## Slide 2
Update on PoA pipeline
Multiple Methodologies/technologies in a PoA
Consideration of Cross effect
Sampling
Post registration change
Start date and crediting period
Multiple country PoAs
Further work
Outline

## Slide 3
Updates on Programme of activities (PoAs)
CME
CER Buyer
CPA
CPA
CPA
CPA
$$$
CME – coordinating or managing entity
CPA – CDM programme activity
Unlimited number of similar component project activities (CPA) can be administered under a single programme umbrella.
Scale up the CDM
  No specified size limits
  CPA can be time bound (e.g. activities commencing in a certain year).
Reduce transaction costs

## Slide 4: Updates on POAs
Source: UNEP DTU/CDM pipeline

## Slide 5: Updates on POAs
Source : UNEP DTU/CDM pipeline

## Slide 6: Requirements for Multiple Methodologies/technologies in a PoA
Use pre approved combinations
For other combinations account for cross effects;
  EB68 “Guidelines for consideration of interactive measures for application of multiple CDM methodologies for PoAs”
  For LSC combination, request clarification/revision to MP
  Min one specific case CPA at time of the publication of the PoA-DD for GSC corresponding to any of the generinc CPA-DDs shall be provided. Specific CPA for other technologies (remaining generic CPA-DDs) can be added at the time of registration of the PoA or after the registration of the PoA. In the latter case, the specific-case CPA-DD shall be provided for approval by the Board in accordance with the post-registration change process.
Notes: Pink text, this is not valid anymore right?

## Slide 7: SSC Pre approved combinations
Combinations of approved methodologies by the Board are contained in the SSC General Guidelines:
  AMS-III.R + AMS-I.C; AMS-III.D + AMS-I.C + AMS-I.F; and
  AMS-I.C + AMS-I.F.
  Any one of the Type III methane generating methodologies, with any one of the Type I methane utilizing methodologies
    i.e. AMS-III.H, AMS-III.D, AMS-III.F and AMS-III.G, with AMS-I.A, AMS-I.C, AMS-I.D and AMS-I.F.
    A generic CPA-DD has been prepared for each technology/measure, each methodology and each combination thereof, or that technologies/measures have been combined in one generic CPA-DD subject to the provisions in the PS.

## Slide 8: Cross effects
EE measures in a building
Activity 1: efficient lighting bulbs
Activity 2: efficient space heating/cooling
Cross effect: Activity 1 will lead to increased/reduced fuel consumption for the same level of space heating/cooling.
Cross effects examples

## Slide 9: Sampling Requirements
  Use the following confidence/precision requirements:
    90/10 for small-scale;
    95/10 for large-scale;
    Unless specified in the applicable methodology;
  For precision (i.e. figure of ±10%), use relative percentage terms when parameter of interest is both a proportion and a mean value;
    ±10% when average usage of a CFL is 3.5 hours implies that the population parameter is to be within ± 0.35hours.
    ±10% when one expects 50% of cook stoves still to be operational means that population value is to be within ± 5%.

## Slide 10: Sampling for a group of CPAs
  Sampling allowed for a group of CPAs under a small scale PoA; populations of all CPAs in the group are combined for a single survey
PoA
CPA 1
CPA 2
CPA 3
CPA 4
CPA 5
Group of CPAs
Notes:   Request for issuance: covers all CPAs included under the PoA
EB 80: A random sub-sample within the common survey is allowed as long as: (i) the reliability specification (e.g. 90/10 confidence/precision for small-scale project activities and 95/10 for large-scale project activities) is achieved for each individual parameter, and (ii) the random sub-sample is consistent with the design of the survey and the corresponding sample size calculation.
Parameter values shall be estimated by sampling in accordance with the requirements in the applied methodology separately and independently for each of the CPAs included in a PoA except when a single sampling plan covering a group of CPAs . Several groups of CPAs may be formed and sample sizes may be calculated for the groups.

## Slide 11: Validation and Verification of Sampling plans of Project Activities and PoAs
  Criteria for Validation of Sampling Plans
    Adequate to achieve confidence/precision requirements? Reproduce of sample size calculation;
    Samples are randomly selected and are representative?
  DOEs may apply sampling when PPs have not applied sampling provided predefined level of assurance is met.

## Slide 12: Sampling for DOE validation/verification
 |  | Producers = 5% Consumers = 5% |  | Producers = 10% Consumers = 10% |  | Producers = 10% Consumers = 20% | 
AQL | UQL | Sample Size (n) | Accept. number (c) | Sample Size (n) | Accept. number (c) | Sample Size (n) | Accept. number (c)
1% | 10% | 61 | 2 | 38 | 1 | 29 | 1
1% | 15% | 30 | 1 | 25 | 1 | 10 | 0
1% | 20% | 22 | 1 | 18 | 1 | 8 | 0
0.5% | 10% | 46 | 1 | 38 | 1 | 16 | 0
0.5% | 15% | 30 | 1 | 15 | 0 | 10 | 0
0.5% | 20% | 22 | 1 | 11 | 0 | 8 | 0
New

## Slide 13: Post registration changes
With regard to the permanent changes to a registered PoA, only the following changes shall be allowed:
Changes to programme boundary to expand geographical coverage or to include additional host Parties;
The following revisions to the eligibility:
(i) If the version of methodologies applied by the PoA is revised or replaced subsequent to being placed on hold;
(ii) If the revision of the eligibility criteria of a registered PoA is initiated by the Board at any time during the lifetime of the PoA if an issue related to environmental integrity is identified;
(iii) If the use of positive lists is introduced based on the “Guidelines on the demonstration of additionality of small-scale project activities” or the provisions of “Guidelines on demonstrating additionality of microscale project activities”;

## Slide 14: Post registration changes
c) If a PoA includes more than one generic CPA-DD, addition of specific case CPA-DDs corresponding to generic CPA-DDs for which a specific case CPA-DD has not been submitted at the time of request for registration of the PoA;
(d) Removal of methodologies and/or standardized baselines from the registered PoA;
(e) Addition or change of technologies/measures with or without addition or change of applied methodologies4 in the registered PoA-DD as follows:
(i) Changes that allow a shift to more efficient less GHG-intensive or at least equivalent technologies/measures;5
(ii) Changes that introduce complementary measures/technologies involving mass and/or energy transfer to/from the originally registered technology/measure (e.g. addition or change of Type I methodologies in a registered PoA primarily applying Type III methodologies)1
1 the scope of changes shall not cover adding technologies/measures and methodologies that are not related to the technologies and methodologies included in the originally registered PoA.

## Slide 15: Start date and crediting period
CPA2
CPA3
CPA4
CPA5
CPA6
PoA lifetime = max. 28 years
Start date of PoA (Date of registration at earliest)
End date of PoA
7yrs
7yrs
7yrs
7 yrs
Renewal CP
CPAs
CPA1
●
●
●
●
●
●
PoA renewal
PoA renewal
PoA renewal
● CPA renewal
Fixed CP
CPAs

## Slide 16: Batched issuance
Monitoring Period i
MR
for Batch A
MR
for Batch B
Iss Req
for Batch A
Iss Req
for Batch B
Monitoring Period i+1
Mutually exclusive
MR
for Batch A
MR
for Batch B
Iss Req
for Batch A
Iss Req
for Batch B
Mutually exclusive
MR
for Batch A
EB78
EB75
Iss Req
for Batch A
PCP186 (b): Iss Req for the subsequent MP shall not be submitted before the CERs were issued for both Iss Req for the specified monitoring period
One issuance request covering all CPAs
Prior to EB75
Notes: Paragraph 64 states that the certification report shall constitute a request for issuance to the Executive Board of CERs equal to the verified amount of reductions of anthropogenic emissions by sources of greenhouse gases.

## Slide 17: Batched issuance
MP 63 recommended to exclude the following list of methodologies from using simplified option approved in EB78 (para 31)
Methodologies containing specific provisions within the methodology (i.e., under the section “Project activity under a programme of activities”) are also excluded.
Where multiple methodologies are used in a PoA which includes at least one methodology listed in the table, the PoA is not eligible for using the flexible option
 | Large scale methodologies
AM0036 | Fuel switch from fossil fuels to biomass residues in heat generation equipment
AM0057 | Avoided emissions from biomass wastes through use as feed stock in pulp and paper, cardboard, fibreboard or bio-oil production
AM0061 | Methodology for rehabilitation and/or energy efficiency improvement in existing power plants
AM0094 | Distribution of biomass based stove and/or heater for household or institutional use
AM0108 | Interconnection between electricity systems for energy exchange
ACM0005 | Increasing the blend in cement production
ACM0006 | Consolidated methodology for electricity and heat generation from biomass
ACM0017 | Production of biodiesel for use as fuel
ACM0018 | Electricity generation from biomass residues in power-only plants
ACM0020 | Co-firing of biomass residues for heat generation and/or electricity generation in grid connected power plants
ACM0022 | Alternative waste treatment processes

## Slide 18
A PoA can be registered with more than one host Party to begin with or a PoA can initially be registered with one host Party but, during its operation, can be expanded to additional host Parties.
  In the former case, the CME shall:
    Obtain a LoA from the DNA of each Party involved in the PoA prior to registration;
    Provide only one specific-case CPA-DD for each generic CPA-DD.
  In the latter case (expanded through post-registration change process), the CME shall:
    Obtain LoAs from the DNAs of the additional host Parties;
    Provide a revised PoA-DD and a revised generic CPA-DD.
Provisions for multi-country PoAs

## Slide 19
Of the 247 registered PoAs, 24 are multi-country PoAs at the registration stage.
In addition, more than 26 registered PoAs have indicated the intention to expand the boundary (adding more host Parties) in the future.
  e.g. Ref: 9626 (Rwanda) will be expanded to Eastern African countries.
Provisions for multi-country PoAs

## Slide 20
    In a multi-country PoA, if technology/measure is the same, it may be interpreted that only one specific-case CPA-DD is required for registering the PoA or for expanding the boundary;
    DNAs have generally required at least one specific-case CPA-DD from their country.
DNAs suggested that it is desirable to amend the PoA rules to require at least one specific-case CPA-DD per host country;
  It would enable a better assessment of sustainable development aspects of the PoA;
  Specific information on inputs from local stakeholders may only be available in a specific-case CPA-DD.
CMEs request simplification of requirements by the Board and DNA.
Provisions for multi-country PoAs

## Slide 21
Currently one specific case CPA-DD per technology/measure is required.
Geographic boundaries, especially when they span multiple countries, may play a role to render some CPAs unique.
  e.g. In a PoA distributing cookstoves or efficient lights, there may be differences among countries regarding infrastructure, population density, cooking habits with impacts on monitoring, project performance and emission reductions
Separate specific-case CPA-DDs per country may provide more accurate case specific information.
Will not be a new requirement for documentation but may indicate that some specific-case CPA-DDs will be required earlier.
Provisions for multi-country PoAs

## Slide 22
The Board agreed to require that the CME should provide a specific-case CPA-DD for each host Party during the registration of the PoA or during expansion of the boundary of the PoA to add additional host Parties.
Provisions for multi-country PoAs

## Slide 23: Ongoing work on PoA regulation
Multi country PoA – (request for review)
Definition of technology
Revision of eligibility criteria by CME (standardizing eligibility criteria)
Post registration changes to PoA
Multiple specific CPA-DD per generic CPA-DD at registration of PoA
Survey requirements to estimate multiple parameters in single survey
More best practice examples for sampling
Sample Size calculator
And more ……

## Slide 24: THANK YOU!
Karen Ortega
Technical Officer,
RCC Bogota
kortega@unfccc.int