NAI Greenhouse Gas Inventory Workshop

Energy Sector – Fugitives Quiz 2

Name:                                                                     .

- Which of the following statements is false:

  - Large facilities are the major contributors of fugitive emissions on both oil and natural gas systems

  - Storage tanks are likely to be significant sources of methane emissions at production facilities

  - Casing gas venting from heavy oil wells is potentially a major source of methane emissions

  - Waste gas is normally only flared if it is highly toxic or odorous, otherwise it is vented

- Which of the following statements is false:

- Any countries that have a natural gas system, oil production or petroleum refining should be reporting vented and flared volumes

- Any gas processing plants that have gas sweetening units will likely have raw CO2 emissions

- All gas processing plants use natural gas as the supply medium for gas operated instruments

- Any plants that process sour natural gas likely have raw CO2 emissions

- None of the above

- Which of the following statements is false:

- Sour waste gas is more apt to be flared than vented

- Shallow wells are less likely to produce sour natural gas than deep wells

- Petroleum refineries tend to contribute more methane emissions from fugitive equipment leaks than do upstream field facilities

- An important consideration in evaluating the amount of emissions from gas distribution systems is the amount of cast iron pipeline

- None of the above

- Storage tanks at pipeline terminals are normally sources of:

- Working losses

- Breathing (or standing) losses

- Flashing losses

- Fugitive equipment leaks

- All of the above

- a and b only

- a, b and c only

- a, b and d only

- Emissions from fugitive equipment leaks are typically unaffected by:

- Type of component

- Type of service

- Industry sector

- Age of facility

- Toxicity or economic value of the process fluid

- None of the above

- Which of the following is not normally a source of venting emissions:

- Heavy oil wells

- Natural gas wells

- Use of natural gas as the supply medium for gas-operated equipment

- Natural gas compressor stations

- Which of the following is not a source of fugitive emissions:

- Process sewers

- Tailings ponds

- API separators

- Emergency vents

- Produced water tanks

- Underground coal fires

- None of the above

# Text boxes

Answer

Answer

Answer

Answer

Answer

Answer

Answer