ANNEX 2

Table 2: GPG2000 good practice in adapting Revised 1996 IPCC Guidelines

to lack of activity data (AD) and emission factors (EFs)

| SUBSOURCE CATEGORY: 2A1 CO2 – CEMENT PRODUCTION |
| --- |
| National circumstance | Recommended Good Practice | Reference |
| Plant level clinker production data not available | Obtain AD from national cement statistics, industry association, or international data sources | Decision Tree Figure 3.1 |
|  | Estimate emissions using Tier 1 method based on cement data based on clinker produced in country |  |
| Cement types are known | Use default fractions for various cement types to estimate clinker fractions in each cement type | Tables 3.1, 3.3A; 3.3B |
| Fraction of cement types not available | Use default fractions (eg 95% clinker for essentially Portland cement (NOTE-98% Default in Rev96GL is considered too high by GPG2000) | GPG2000 page 3.14 para 1 |
| CaO content of clinker not available | Use default lime (CaO) content value of 65% |  |
|  | EMISSION FACTOR ESTIMATION |  |
| Country-specific EF not developed and documented | Estimate EF emissions based on Equation 3.3 (EF=0.785tonneCO2/tonne pure lime×CaO pure lime /tonne pure clinker)×f pure clinker/total clinker (with other non-carbonaceous materials (eg gypsum CaSO4) | GPG2000 page 3.12 |
|  | PROCESS EMISSIONS ESTIMATION (Tier 1) |  |
| Process emissions not estimated for lack of EF | For Portland cement : EF=stoichiometric ratio (0.785)×Default lime content in clinker depending on cement type(s) (CaO)×Default clinker ratio (f) |  |
|  | Where: Stiochiometric ratio=0.785tonneCO2/tonne pure Default lime content in clinker=0.65 pure lime/tonne pure clinker Default clinker ratio=0.95pure clinker/tonne total clinker |  |
|  | =0.785tonneCO2/tonne pure limex0.65 pure lime/tonne pure clinker×0.95pure clinker/tonne total clinker |  |
|  | =0.485 tonne CO2/tonne total clinker |  |
| UNCERTAINTIES | Default provided based on the Decision Tree | Table 3.2 |
| quality assurance/ quality control (QA/QC) | Source category specific QA/QC procedures | Section 3.1.1.3 |
|  | Comparison of top-down and any bottom-up approaches |  |
|  | Compare aggregated national factors (where available) and IPCC(D) and document differences |  |
|  | Site-specific activity data checks at plant-level for measurement techniques, technology type, operational practices and data reporting system |  |

Table 2.2

| SUBSOURCE CATEGORY: 2A2: CO2 – LIME PRODUCTION |
| --- |
| National circumstance | Recommended Good Practice | Reference |
| Plant-level lime production data not available | Estimate total production from national statistics, industry association, international data | Decision Tree Figure 3.2 |
|  | Include estimate of commercial and captive lime production from other sources, eg. iron and steel plants |  |
| Fractions (purity) of lime types not available | Use default CaO and CaOMgO fractions (purity) | Table 3.4 |
|  | f (quick lime)=0.95 tonne pure CaO/tonne total lime | GPG2000 Table 3.4 |
|  | f (dolomite)=0.85/95tonne CaOMgO /tonne total dolomite |  |
|  | f (hydraulic lime=0.75 tonne CaO/tonne total hydraulic |  |
| Country-specific EFs not developed | EF ESTIMATION METHOD |  |
|  | EF (by lime type) = stoichiometric ratio (lime type)×purity factors (f) (by lime type) |  |
|  | Estimate component lime EFs |  |
|  | EF(quick lime)=0.785×f(1) =0.785×0.95=0.75 | GPG2000 Table 3.4 |
|  | EF(dolomite lime)= 0.913×f(2) =0.913×0.85=0.776 |  |
|  | EF(hydraulic lime) =0.785× f(3) =0.785×0.75=0.589 |  |
| Fractional composition of lime not available | Default ratio 85/15 | GPG2000 page 3.22 para. 4 |
|  | Estimate aggregate EF based on fractions of lime types using equations 3.5A and 3.5B |  |
|  | EF(aggregate): |  |
|  | = p×EF(quick lime)+ q×EF(dolomite) |  |
|  | where p,q are proportions/lime fractions by type | GPG2000 page 3.20 |
|  | =0.85×0.75+0.15×0.78 = 0.75 (Aggregate EF) (Stoichiometric ratio=0.79) |  |
|  | PROCESS EMISSIONS ESTIMATION |  |
|  | CO2 Emissions = Aggregate EF tonne/tonne total aggregate Lime × AD tonne total aggregate lime |  |
| Production of hydrated lime not available | Apply default ratio of hydrated lime | Table 3.5 |

| SUBSOURCE CATEGORY: CO2-Iron and Steel production |
| --- |
| National circumstance | Recommended Good Practice | Reference |
| Data on reducing agents or plant-specific information on fuels used as reducing agent (CO, H2, natural gas) not available | Use nationally compiled production data on iron/steel production: | Decision Tree Figure 3.3 |
| Country-specific methodology not developed and/or documented | Estimate emissions based on Tier 1 method as follows: |  |
|  | ESTIMATE AD FOR REDUCING AGENTS BASED ON PROCESS REACTION |  |
|  | Process Reaction: |  |
|  | Fe2O3 + 3C = 2Fe + 3/2 CO2 |  |
|  | Stoichiometric ratio = 36 tonnes C/ X tonnes of pig Iron |  |
|  | Estimate mass of reducing agent from coke and charcoal consumption based on stoichiometry of iron ore reduction in integrated iron and steel industry production including EAF electrodes where applicable |  |
|  | AD (Mass of reducing Agent) = 36 tonnes C/X tonnes pig iron × Q total pig iron production |  |
| Lack of EF | Use DEFAULT EF by reducing agent type |  |
|  | Coal | 2.5 tonne CO2/tonne reducing agent | Table 2-12 Rev96GL |
|  | Coke | 3.1 tonne CO2/tonne reducing |  |
|  | Petrol coke | 3.6 tonne CO2/tonne reducing agent |  |
| Source category not estimated (NE) | PROCESS EMISSIONS ESTIMATION |  |
|  | Estimate emissions based on mass of reducing agents using default EFs | GPG2000 Table 3.6 |
|  | CO2 emissions = EF tonnes CO2/tonne reducing agent C(type) × AD tonne C(type) |  |
|  | Subtract fuels used as reducing agent from 1A1–fuel combustion subsource to avoid double counting | Decision Tree 3.3 Box 1 |
|  | Note: The method overestimates net CO2 emissions by the neglect of carbon storage steel production (Default mass storage C = 2.5-3.5 kg/tonne steel) | Rev96GL section 2.13.3.2 |
| SUBSOURCE CATEGORY: 2B3: N2O –NITRIC ACID PRODUCTION |
| National circumstance | Recommended Good Practice | Reference |
| Plant-specific emissions and destruction data not available directly from plants |  |  |
| Plant-specific production data (AD) and EF not available | Use aggregate production data from national statistics, industry association, international data |  |
|  | Identify the origin of the design (Canada, USA, Japan, Norway) to select appropriate default N2O generation factor | Table 3.8 |
|  | Identify nitric acid intermediate production that may be integrated in other process plants and not reported as commercial product to improve completeness (coverage). Generally these constitute about 30–50% of reported production. | Completeness page 3.36 |
| SUBSOURCE CATEGORY: 2B4: N2O – Adipic Acid production |
| National circumstance | Recommended Good Practice | Reference |
| Plant-specific emissions and destruction data not available directly from plants | Use aggregate production data from national statistics, industry association, international data |  |
| Plant-specific production data (AD) and EF not available | identify the abatement technologies and utilisation factor to select appropriate Default N2O generation factor | Table 3.7 |
| SUBSOURCE CATEGORY: 2C4: PFCs – Aluminium production |
| National circumstance | Recommended Good Practice | Reference |
| Where smelter level process data (AEF, AED/AEO) are not available | Use default emission factors by technology type for CF4 and CF6 separately | GPG2000 Table 3.10 |
|  | Estimate emissions using default EF (kg/tonne Al) multiplied by the aluminium production over time |  |