## Slide 1: IPCC Inventory Software: IPPU Updates
IPCC TFI Side-event
UNFCCC COP27
Sharm el-Sheikh, Egypt
November 2022

## Slide 2: IPPU Main Updates
Implementation of higher Tiers
  Higher Tiers mean more disaggregated data are needed, i.e. technology-specific EFs and plant-specific data
  A user may use a mix of Tiers within the same category
Introduction of a category subdivisions (e.g. national, region, plant, etc.)
  A user can enter a single subdivision (e.g., a national level) or many user-defined sub-divisions (e.g., prefectures or facilities)
More possibilities to select user-defined technologies, production processes and materials
  Users can disaggregate each category according to its national circumstances according to country-specific technologies, production processes and input materials, and to enter country- or plant-specific values (EFs and parameters)

## Slide 3: Example of a Worksheet
Sub-divisions
Worksheets Menu (Tiers)
Default or User-defined process/technology
Default or User-defined parameter

## Slide 4: IPPU Worksheets
IPCC Category | Number of Worksheets
2 - Industrial Processes and Product Use (IPPU) | 
2.A - Mineral Industry | 28
2.B - Chemical Industry | 89
2.C - Metal Industry | 38
2.D - Non-Energy Products from Fuels and Solvent Use | 3
2.E - Electronics Industry | 24
2.F - Product Uses as Substitutes for Ozone Depleting Substances | 21
2.G - Other Product Manufacture and Use | 42
2.H - Other | 6
 | 251

## Slide 5: 2.A Mineral Industry
IPCC Category | Number of Worksheets | Number of Worksheets |  |  | 
 | Total | IPCC Tiers |  |  | 
IPCC Category |  | Tier 1 |  | Tier 2 | Tier 3
2.A - Mineral Industry |  |  |  |  | 
2.A.1 - Cement production | 8 | 2 (cement AD, ExIm, default EF) |  | 1 (clinker AD, CKD) | 4 (plant-specific AD, emissions total)
 |  | 1 (capture/reduction for all Tiers) |  |  | 
2.A.2 - Lime production | 6 | 1 (default EFs) |  | 1 (LKD, correction) | 3 (plant-specific AD)
 |  | 1 (capture/reduction) |  |  | 
2.A.3 - Glass Production | 3 | 1 (worksheet for Tier 1 and 2) |  |  | 1 (for each furnace)
 |  | 1 (capture/reduction) |  |  | 
2.A.4 - Other Process Uses of Carbonates |  |  |  |  | 
2.A.4.a - Ceramics | 2 | 2 (worksheets can be used for all Tiers: Tier 1 – defaults, Tier 2 – data on limestone/dolomite use, Tier 3 – carbonates AD, calcination) |  |  | 
2.A.4.b - Other Uses of Soda Ash | 2 | 2 (worksheets can be used for all Tiers, same as 2A4a) |  |  | 
2.A.4.c - Non Metallurgical Magnesia Production | 2 | 2 (worksheets can be used for all Tiers, same as 2A4a) |  |  | 
2.A.4.d - Other (please specify) | 3 | 2 (worksheets can be used for all Tiers, same as 2A4a), 1 (for reporting issues) |  |  | 
2.A.5 - Other (please specify) | 2* |  | 2 (1 generic worksheet AD x EF, 1 capture/reduction) |  | 
* Implements generic equation (AD x EF). No default values are provided in the 2006 IPCC Guidelines

## Slide 6: 2.B Chemical Industry
IPCC Category | Number of Worksheets |  |  | 
 | Total | IPCC Tiers |  | 
IPCC Category |  | Tier 1 | Tier 2 | Tier 3
2.B - Chemical Industry |  |  |  | 
2.B.1 - Ammonia Production | 2 | 2 (1 for all Tiers, where Tier 3 plant-specific, 1 for capture/reduction) |  | 
2.B.2 - Nitric Acid Production | 3 | 1 (AD x EF) | 1 (AD x EF plus abatement) | -- (measurements)
 |  | 1 (capture/reduction) |  | 
2.B.3 - Adipic Acid Production | 3 | 1 (same as 2.B.2) | 1 (same as 2.B.2) | -- (measurements)
 |  | 1 (capture/reduction) |  | 
2.B.4 - Caprolactam, Glyoxal and Glyoxylic Acid Production | 3 | 1 (same as 2.B.2) | 1 (same as 2.B.2) | -- (measurements)
 |  | 1 (capture/reduction) |  | 
2.B.5 - Carbide Production | 3 | 3 (for all Tiers same equation, where Tier 3 plant-specific data.1 worksheet for carbide production, 1 for carbide use in acetylene, 1 for capture/reduction ) |  | 
2.B.6 - Titanium Dioxide Production | 3 | 1 (AD x EF) | 1 (carbon content and oxidation) | -- (no Tier 3)
 |  | 1 (capture/reduction) |  | 
2.B.7 - Soda Ash Production | 2 | 2 (same equation for two tiers, 1 worksheet for capture/reduction) |  | -- (measurements)

## Slide 7: 2.B Chemical Industry - Petrochemicals
IPCC Category | Number of Worksheets | Number of Worksheets |  | 
 | Total | IPCC Tiers |  | 
IPCC Category |  | Tier 1 | Tier 2 | Tier 3
2.B.8 - Petrochemical and Carbon Black Production |  |  |  | 
2.B.8.a - Methanol | 9 | 1 (AD, feedstock, technologies) |  | 4 (combustion, flares, vents + CH4 atm.measurement)
 |  | 2 (1 for CO2, 1 for CH4) | 1 (only CO2, mass-balance approach) | 
 |  | 1 (capture/reduction) |  | 
2.B.8.b - Ethylene | 9 | 2 | 1 | 4
 |  | 1 |  | 
 |  | 1 |  | 
2.B.8.c - Ethylene Dichloride and Vinyl Chloride Monomer | 9 | 2 | 1 | 4
 |  | 1 |  | 
 |  | 1 |  | 
2.B.8.d - Ethylene Oxide | 9 | 2 | 1 | 4
 |  | 1 |  | 
 |  | 1 |  | 
2.B.8.e - Acrylonitrile | 9 | 2 | 1 | 4
 |  | 1 |  | 
 |  | 1 |  | 
2.B.8.f - Carbon Black | 9 | 2 | 1 | 4
 |  | 1 |  | 
 |  | 1 |  | 
The same guidance for all 2.B.8 sub-categories – 2.B.8. a, b, c, d, e, f

## Slide 8: 2.B Chemical Industry - Fluorochemicals
IPCC Category | Number of Worksheets |  |  |  | 
 | Total | IPCC Tiers |  |  | 
IPCC Category |  | Tier 1 | Tier 2 | Tier 3 | 
2.B.9 - Fluorochemical Production |  |  |  |  | 
2.B.9.a - By-product emissions | 12 | 2 (1 for HFC-23, 1 for other F-gases) | 1 (for HFC-23 based on efficiencies) | 8 (1 for HFC-23 direct method, 2 for HFC-23 proxy method, 2 HFC-23 monitoring method, 1 for other F-gases direct, 2 for others proxy method ) | 8 (1 for HFC-23 direct method, 2 for HFC-23 proxy method, 2 HFC-23 monitoring method, 1 for other F-gases direct, 2 for others proxy method )
 |  | 1 (capture/reduction) |  |  | 
2.B.9.b - Fugitive Emissions | 2 | 2 (for all others, 1 capture/reduction) | [under development] |  | 
2.B.10 - Other (Please specify) | 2* |  | 2 (1 generic worksheet AD x EF, 1 capture/reduction) |  | 

## Slide 9: 2.C Metal Industry
IPCC Category | Number of Worksheets |  |  | 
 | Total | IPCC Tiers |  | 
IPCC Category |  | Tier 1 | Tier 2 | Tier 3
2.C - Metal Industry |  |  |  | 
2.C.1 - Iron and Steel Production | 9 | 2 (1 for Iron&Steel, 1 for Coke in Energy – CO2, CH4 EF) | 6 (2 for Coke in Energy, 1 for Iron&Steel, 1 for Sinter, 1 for Pellets, 1 for DRI – CO2 mass-balance) | -- (plant-specific data and measurements)
 |  | 1 (capture/reduction) |  | 
2.C.2 - Ferroalloys Production | 9 | 1 (AD x EF) | 1 (for reducing agents EF) | 1 (for reducing agents CC)
 |  |  | 5 (ore, slag, products, non-products, summary) | 
 |  | 1 (capture/reduction) |  | 
2.C.3 - Aluminium production | 9 | 2 (1 for CO1, 1 for PFCs) | 6 (for Tier 2/3 for CO2 for Soderberg and Prebake, and for PFCs for Slope and Overvoltage) | 
 |  | 1 (capture/reduction) |  | 
2.C.4 - Magnesium production | 5 | 2 (1 for CO1, 1 for SF6) | 2 (1 for CO1, 1 for SF6) | -- (measurements)
 |  | 1 (capture/reduction) |  | 
2.C.5 - Lead Production | 2 | 2 (1 AD x EF, 1 capture/reduction) | -- (mass-balance of CC) | -- (measurements)
2.C.6 - Zinc Production | 2 | 2 (same as 2.C.5) | -- (same as 2.C.5) | -- (same as 2.C.5)
2.C.7 - Other (please specify) | 2* |  | 2 (1 generic worksheet AD x EF, 1 capture/reduction) | 

## Slide 10: 2.D Non-Energy Products from Fuels 2.E Electronics Industry
IPCC Category | Number of Worksheets |  |  | 
 | Total | IPCC Tiers |  | 
IPCC Category |  | Tier 1 | Tier 2 | Tier 3
2.D - Non-Energy Products from Fuels and Solvent Use |  |  |  | 
2.D.1 - Lubricant Use | 1 | 1 (1 worksheet for default and CS EFs) |  | -- (no Tier 3)
2.D.2 - Paraffin Wax Use | 1 | 1 (1 worksheet for default and CS EFs) |  | 
2.D.3 - Solvent Use | -- (no guidance) |  |  | 
2.D.4 - Other (please specify) | 1 | 1 (generic guidance AD x EF) |  | 
2.E - Electronics Industry |  |  |  | 
2.E.1 - Integrated Circuit or Semiconductor | 7 | 1 (AD x EF) | 6 (2 for managers: F-gas and by-products, 2 for Tier 2a: F-gas and by-products, 2 for Tier 2b: F-gas and by-products) | -- (plant-specific data)
2.E.2 - TFT Flat Panel Display | 7 | 1 (same as 2.E.1) | 6 (same as 2.E.1) | 
2.E.3 - Photovoltaics | 7 | 1 (same as 2.E.1) | 6 (same as 2.E.1) | 
2.E.4 - Heat Transfer Fluid | 2 | 1 (EF approach) | 1 (mass-balance approach) | -- (no Tier 3)
2.E.5 - Other (please specify) | 1* |  | 1 (generic worksheet AD x EF) | 

## Slide 11: 2.F Product Uses as Substitutes for ODS
IPCC Category | Number of Worksheets |  |  | 
 | Total | IPCC Tiers |  | 
IPCC Category |  | Tier 1 | Tier 2 | Tier 3
2.F - Product Uses as Substitutes for Ozone Depleting Substances (ODS) |  |  |  | 
2.F.1 - Refrigeration and Air Conditioning |  |  |  | 
2.F.1.a - Refrigeration and Stationary Air Conditioning | 4 | 1 (default/spreadsheet model, Tier 1a/b) | 3 (1 for parameters, 1 for Tier 2a EF-approach, 1 for Tier 2b mass-balance) | -- (no Tier 3)
2.F.1.b - Mobile Air Conditioning | 4 | 1 (same as 2.F.1a) | 3 (same as 2.F.1a) | 
2.F.2 - Foam Blowing Agents | 6 | 2 (default/spreadsheet, 1 for closed cells, 1 for open cells) | 4 (2 for open cell parameters and Tier 2 estimation, 2 for closed cell parameters and estimation) | 
2.F.3 - Fire Protection | 1 | 1 (default/spreadsheet) | -- (no Tier 2 and Tier 3) | 
2.F.4 - Aerosols | 1 | 1 (default and CS application and data) |  | -- (no Tier 3)
2.F.5 - Solvents | 3 | 1 (default) | 2 (1 for parameters, 1 for estimation) | 
2.F.6 - Other Applications (please specify) | 2 | 2 (1 for emissive applications, 1 for contained applications) | -- (no Tier 2 and Tier 3) | 

## Slide 12: 2.G Other Product Manufacture and Use (1)
IPCC Category | Number of Worksheets |  |  | 
 | Total | IPCC Tiers |  | 
IPCC Category |  | Tier 1 | Tier 2 | Tier 3
2.G - Other Product Manufacture and Use |  |  |  | 
2.G.1 - Electrical Equipment | 1 | -- (at the level of category 2.G.1 only Tier 3 method can be used which is mass-balance for utility level) |  | 1
2.G.1.a - Manufacture of Electrical Equipment | 9 | 1 (default and country-specific) |  | 7 (3 for mass-balance, 4 for EF approach)
 |  | 1 (capture/reduction) |  | 
2.G.1.b - Use of Electrical Equipment | 4 | 1 (default and country-specific) |  | 2 (1 for mass-balance, 1 for EF approach)
 |  | 1 (capture/reduction) |  | 
2.G.1.c - Disposal of Electrical Equipment | 9 | 1 (default) | 1 (specific for disposal) | 6 (3 for mass-balance, 3 for EF approach)
 |  | 1 (capture/reduction) |  | 
2.G.2 - SF6 and PFCs from Other Product Uses |  |  |  | 
2.G.2.a - Military Applications | 3 | 1 (AD x EF) | 1 (mass-balance) | -- (no Tier 3)
 |  | 1 (capture/reduction) |  | 
2.G.2.b - Accelerators | 4 | 1 (default) | 1 (by accelerator) | 1 (mass-balance)
 |  | 1 (capture/reduction) |  | 
2.G.2.c - Other (please specify) | 4 | 4 (1 for adiabatic uses, 1 for sound-proof glazing, 1 for other applications, 1 for capture/reduction) | -- (no Tier 2 and Tier 3) | -

## Slide 13: 2.G Other Product Manufacture and Use (2)
IPCC Category | Number of Worksheets |  |  | 
 | Total | IPCC Tiers |  | 
IPCC Category |  | Tier 1 | Tier 2 | Tier 3
2.G - Other Product Manufacture and Use |  |  |  | 
2.G.3 - N2O from Product Uses |  |  |  | 
2.G.3.a - Medical Applications | 2 | 2 (1 for estimation based on quantities in Years T and T-1, 1 for capture/reduction) | -- (no Tier 2 and Tier 3) | 
2.G.3.b - Propellant for pressure and aerosol products | 2 | 2 (same as 2.G.3.a) |  | 
2.G.3.c - Other (Please specify) | 2 | 2 (same as 2.G.3.a) |  | 
2.G.4 - Other (Please specify) | 2* |  | 2 (1 generic worksheet AD x EF, 1 capture/reduction) | 

## Slide 14: 2.H Other
IPCC Category | Number of Worksheets | Number of Worksheets |  | 
 | Total | IPCC Tiers |  | 
IPCC Category |  | Tier 1 | Tier 2 | Tier 3
2.H - Other |  |  |  | 
2.H.1 - Pulp and Paper Industry | 2* |  | 2 (1 generic worksheet AD x EF, 1 capture/reduction) | 
2.H.2 - Food and Beverages Industry | 2* |  | same as 2.H.1 | 
2.H.3 - Other (please specify) | 2* |  | same as 2.H.1 | 
* Implements generic equation (AD x EF). No default values are provided in the 2006 IPCC Guidelines
(NMVOCs emissions from Pulp and Paper Industry and Food and Beverage Industry in the Revised 1996 IPCC Guidelines)

## Slide 15: Summary
All IPPU methods provided in the 2006 IPCC Guidelines are implemented in the IPCC Inventory Software (i.e. all equations in Volume 3 of the 2006 IPCC Guidelines)
Flexibility of the IPCC Inventory Software to meet national circumstances is ensured (as per a Tiered approach)
Sub-national reporting allows tracking specific activities/emissions within a national GHG inventory
The Guidebook for IPPU sector to guide users in implementing each and every IPCC method in IPPU is under preparation

## Slide 16: Thank you Users’ feedback is most welcome! Please provide it at: ipcc-software@iges.or.jp